## Slide 1
JWST status, timeline and GO policies
Pierre Ferruit (ESA JWST project scientist)
INAF JWST info day – 17 March 2017
JWST is an international partnership between NASA, ESA and the CSA.

## Slide 2: Contents of the JWST presentation
Mission overview in 6 slides
Mission status
Status – Hardware.
Status – Schedule to launch.
JWST capabilities
Quick overview – imaging, spectroscopy and coronagraphy.
Miscellaneous (moving targets, parallel observations).
Scientific timeline
Timeline for JWST cycle 1.
The Early Release Science (ERS) call.
The timeline for the call for JWST Guaranteed Time Observers (GTOs).
Full timeline including the call for JWST General Observers (GOs).
Conclusion

## Slide 3: Acknowledgements
All along this presentation you will see results from work conducted by a large number of teams in Europe, USA and Canada.
Many elements of this presentation are based on existing presentations prepared by other members of the JWST project, the instrument teams and STScI.
A lot of material used in this presentation is coming from from STScI’s JWST web sites (main resources for getting information):
https://jwst.stsci.edu/ (main site)
https://jwst-docs.stsci.edu/ (documentation site, work in progress)

## Slide 4: JWST mission overview in 6 slides
JWST will be one of the “great observatories” of the next decade.
Often presented as the next step after the Hubble Space Telescope (HST).
Joint mission between NASA, ESA and CSA.
High-priority endeavor for the associated astrophysical communities.
Setup similar to the HST one.
Over the duration of the mission, at least 15% of the total JWST observing time goes to ESA member states applicants.
To be launched in October 2018 for a minimum mission duration of 5 years (10-year goal).

## Slide 5: JWST mission overview in 6 slides

## Slide 6: JWST mission overview in 6 slides
The past and future of astroPAH research - Noordwijk - 31 October 2016
the telescope
secondary mirror
(0.74m diameter)
segmented primary mirror
(18 hexagonal mirrors of 1.32m flat-to-flat; collecting surface > 25m2)
payload module
the 4 instruments and their electronic boxes
the spacecraft
Allows passive cooling of the telescope and the instruments down to ~40K, the size of a tennis court
the spacecraft bus and solar panels
(4 optical elements, only 2 visible here)
Note that a cryogenic cooler is used to cool JWST’s mid-infrared instrument (MIRI) down to 6-7K.
the sunshield

## Slide 7: JWST mission overview in 6 slides
The past and future of astroPAH research - Noordwijk - 31 October 2016
the spacecraft bus and solar panels
Note that a cryogenic cooler is used to cool JWST’s mid-infrared instrument (MIRI) down to 6-7K.

## Slide 8: JWST mission overview in 6 slides
MIRI = Mid-InfraRed Instrument - PIs: G. Wright and G. Rieke
50/50 partnership between a nationally funded consortium of European institutes (MIRI EC) + ESA and NASA/JPL.
NIRSpec = Near-infrared Spectrograph
Provided by the European Space Agency. Built for ESA by an industrial consortium led by Airbus Defence and Space.
NIRISS = Near-infrared Imager and Slit-less Spectrograph
FGS = Fine Guidance Sensor - PIs: R. Doyon & C. Willott
Provided by the Canadian Space Agency.
NIRCam = Near-InfraRed Camera - PI: M. Rieke
Developed under the responsibility of the University of Arizona.

## Slide 9: JWST mission overview in 6 slides
Artist view – R. Hurt
Artist view – D. Hardy
Hubble Ultra-deep Field
Sketch - P. Geil
The end of the dark ages: first light and re-ionization.
The assembly of galaxies: the formation and evolution of galaxies.
The birth of stars and proto-planetary systems.
Planetary systems (including our solar system and exoplanets) and the origin of life.
See Gardner et al., 2006, Space Science Reviews,123, 485

## Slide 10: Status – Hardware - OTIS
OTIS = telescope + instruments
  OTIS = Optical Telescope and Integrated Science instruments module.
2015 and 2016 were very busy years with a lot of very visible progress.
Completion of the integration of OTIS
Start of the environmental test campaign of OTIS.
Extensive and very successful preparation for the cryogenic testing of OTIS at the Johnson space center.
  Make sure the facilities, the test setup, the procedure and the personnel are ready for the actual test.

## Slide 11: Status – Hardware - OTIS
At the beginning of 2016 the payload module of JWST (ISIM = Integrated Science Instrument Module) was ready, fully integrated and tested.

## Slide 12: Status – Hardware - OTIS
Around the same time, the telescope itself (OTE = Optical Telescope Element) was integrated and ready to receive ISIM on its back.

## Slide 13: Status – Hardware - OTIS
JWST OTE
Credit: NASA/Chris Gunn

## Slide 14: Status – Hardware - OTIS
In May 2016, the payload module was installed on the back of the OTE.
Credit: NASA/Chris Gunn

## Slide 15: Status – Hardware - OTIS
In Fall 2016, OTIS integration was successfully completed and ready for environmental testing.
Credit: NASA/Chris Gunn

## Slide 16: Status – Hardware - OTIS
Credit: NASA/Chris Gunn

## Slide 17: Status – Hardware - OTIS
Credit: NASA/Chris Gunn
Vibration testing
Acoustic
testing

## Slide 18: Status – Hardware - OTIS
Credit: NASA/Chris Gunn
Vibration and acoustic testing of OTIS have just been completed.
OTIS is back in the clean room for post-test checks before being shipped to Houston for the cryogenic testing.

## Slide 19: Status – Hardware - sunshield
In parallel to the work on OTIS, the manufacturing of the sunshield hardware continued and we are now mainly in the integration phase.
Credit: Northrop - Grumman
Last flight sunshield layer delivered in Sep. 2016.

## Slide 20: Status – Hardware - sunshield
Credit: Northrop - Grumman
Structure supporting and protecting the folded sunshield during launch.

## Slide 21: Status – Hardware - sunshield
Credit: Northrop - Grumman

## Slide 22: Status – Hardware - spacecraft
The spacecraft is also progressing well and is in its integration phase.
Credit: Northrop - Grumman
RWA = reaction wheel assemblies

## Slide 23: Status – Schedule and contingency
JWST is on track for a launch in October 2018 with almost 5 months of contingency.
Does this mean that we do not encounter any problem?
Of course not. But we have the necessary schedule and funding contingencies to tackle them.

## Slide 24: JWST capabilities

## Slide 25: JWST capabilities

## Slide 26: JWST capabilities (imaging)
Instrument | Wavelength (in microns) | Pixel scale (in mas/pixel) | Field of view (arcmin x arcmin)
NIRCam | 0.6-2.3 | 32 | 2.2’ x 4.4’
NIRCam | 2.4-5.0 | 65 | 2.2’ x 4.4’
NIRISS | 0.9-5.0 | 65 | 2.2’ x 2.2’
MIRI | 5.0-28 | 110 | 1.3’ x 1.7’
More than one order of magnitude sensitivity improvement in some bands.
Extremely powerful observatory, a lot of discovery space.
NIRCam: Simultaneous imaging of the same field of view in the ‘blue’ and ‘red’ channels.

## Slide 27: JWST capabilities (spectroscopy)
Take-home message: in JWST, spectroscopy comes in many different flavors…
NIRCam: Simultaneous imaging of the same field of view in the ‘blue’ and ‘red’ channels.
Instrument | Type | Wavelength (microns) | Spectral resolution | Field of view
NIRISS | slitless | 1.0-2.5 | ~150 | 2.2’ x 2.2’
NIRCam | slitless | 2.4-5.0 | ~2000 | 2.2’ x 2.2’
NIRSpec | MOS | 0.6-5.3 | 100/1000/[2700] | 9 square arcmin.
NIRSpec | IFU | 0.6-5.3 | 100/1000/2700 | 3” x 3”
MIRI | IFU | 5.0-28.8 | 2000-3500 | >3” x >3.9”
NIRSpec | SLIT | 0.6-5.0 | 100/1000/2700 | Single object
MIRI | SLIT | 5.0-10.0 | 60-140 | Single object
NIRSpec | Aperture | 0.6-5.3 | 100/1000/2700 | Single object
NIRISS | Aperture | 0.6-2.5 | 700 | Single object

## Slide 28: JWST capabilities (coronagraphy)
Variety of modes covering the complete wavelength range of JWST.
Instrument | Wavelength (in microns) | Pixel scale (in mas/pixel) | Field of view | Type
NIRCam | 0.6-2.3 | 32 | 20” x 20” | Lyot
NIRCam | 2.4-5.0 | 65 | 20” x 20” | Lyot
NIRISS | 3.8-4.8 | 65 | 0.1-0.5” | Aperture masking interferometry
MIRI | 10.65 | 110 | 24” x 24” | 4QPM
MIRI | 11.4 | 110 | 24” x 24” | 4QPM
MIRI | 15.5 | 110 | 24” x 24” | 4QPM
MIRI | 23 | 110 | 30” x 30” | Lyot

## Slide 29: JWST capabilities - Miscellaneous
JWST can observe moving targets.
Up to 30 mas/s. Covers a lot of the potential Solar System targets.
The cycle-1 calls for proposals will al include the possibility to request for coordinated parallel observations.  great news!

## Slide 30: Scientific timeline – cycle 1
JWST will launch in October 2018
After launch, JWST will deploy (duration ~2-3 weeks) as it cruises toward the Lagrange 2 point.
It will take it ~1 months to reach the vicinity of the Lagrange 2 point around which it will orbit (halo orbit).
  The commissioning should be completed 6 months after launch, i.e. in April 2019.
  Cycle 1 is scheduled to start in April-May 2019.
  Scientific observations will start as soon as possible, mode per mode.
  Full calibration will be achieved progressively during cycle 1.

## Slide 31: Scientific timeline – cycle 1 calls
The first JWST cycle-1 calls have been issued!!!
  JWST guaranteed time observer (GTO) call for proposals.
    https://jwst-docs.stsci.edu/display/JSP/JWST+Cycle+1+Guaranteed+Time+Observations+Call+for+Proposals
  Call for (mandatory) notice of intents for the Early Release Science (ERS) programs.
    https://jwst-docs.stsci.edu/display/JSP/JWST+Director%27s+Discretionary+Early+Release+Science+Call+for+Proposals
The call for general observers (GOs) is planned for November 2017.
  After the GTO proposals are known and the ERS proposals selected.

## Slide 32: Scientific timeline – ERS
The ERS program is based on director’s discretionary (DD) time.
It will have its own selection committee set up by the STScI director.
Specific goals.
  https://jwst.stsci.edu/science-planning/early-release-science-program

## Slide 33: Scientific timeline – ERS
The ERS proposal submission is a two-step process
Mandatory notices of intent & proposals.
We are here

## Slide 34: Scientific timeline – ERS
The mandatory notices of intent to propose (> 200) have been received.
Good presence of European scientists and of Italian ones.

## Slide 35: Status – Scientific timeline – GTO
The GTO proposal submission is a staggered process extending over most of 2017.
We are almost here

## Slide 36: Scientific timeline - full
In the background, a lot of work to get the tools and the documentation ready.
The GTOs and the ERS proposers will try the system.
A lot of additional material will be available for the cycle-1 GO call.

## Slide 37: Scientific timeline - full

## Slide 38: More opportunities to prepare…
“Science with the Hubble & James Webb space telescopes V” in Venice (20-24 march 2017).
  A 1-day workshop at the end.
Special session “Preparing the JWST era” at the EWASS 2017.
  Focusing on learning from the GTO proposals (transferring experience). Work in progress.
Second JWST ESAC workshop “Mastering the science instruments and of the observing modes of JWST [get set]” at ESAC (4-6 October 2017).
  Following the successful [on your mark] 2016 edition.
Workshop “Planning Solar System Observations with JWST” in ESTEC (13-15 December 2017).
  Mirroring a similar US workshop planned for November.

## Slide 39: Conclusion
Launch in October 2018 (stable) and we can now say we launch next year!
Some cycle-1 calls for proposals have been issued and the call for GOs will be issued this year also!
Thanks for your attention