## Slide 1: Detectors of JWST Near IR Instruments
Marco Sirianni
ESAC 2016 JWST Workshop
ESAC, September 26-28, 2016

## Slide 2: JWST NIR detectors
All JWST NIR Instruments uses one or more Teledyne
HgCdTe 2048x2048 18mm pixel detectors (H2RG)
Hybrid CMOS architecture:
  HgCdTe detector layer
    2.5mm or 5.3 mm wavelength cutoff
  Silicon Readout integrated circuit (ROIC)
    multiplexing
Each detector is controlled by a dedicated Teledyne
programmable SIDECAR ASIC
  Provides clock and biases to the detector
  Provides 16 Bit A2D conversion
  Transmits digital data to the Instrument detector electronics
Each ASIC-detector pair is “tuned” for optimal performance

## Slide 3: SCAs and FPAs
Each detector is called Sensor Chip Assembly (SCA)
The Focal Plane Array (FPA) of a given SI can have one or more SCAs
Instrument | FPA/SCA | l cutoff
NIRISS | 1 / 1 | 5.3
NIRCam | 2 / 4 2 / 1 | 2.5 5.3
NIRSpec | 1 / 2 | 5.3
NIRSpec FPA
NIRcam LW FPA (1 of 2)
NIRcam SW FPA (1 of 2)

## Slide 4: Anatomy of a SCA
JWST H2RG read out using 4 outputs, each one taking care of a 512x2048 region
Pixels are continuously clocked at 100Khz rate to hold power dissipation constant
2048x2048 pixel array
2040x2040 sensitive area
4 rows and columns or reference pixels on each side to track electronic bias and temperature drifts to correct science data
4 rows and columns or reference pixels
2040
2040
The four outputs are operated in parallel
The ASIC re-order the pixels
I/O pads

## Slide 5: Readout Modes
j
Vertical slow scanning direction
VDIR=0
Horizontal fast scanning direction
HDIR=0
HDIR=0
HDIR=1
HDIR=1
i
Standard Full Frame Readout
4 outputs
10.73 seconds to read the frame
Subarray mode
1 single outputs
Rules on size of window:
  Min NCOLS, NROWS=8
  NCOLSxNROWS = multiple of 64
Frame time depends on size
(2ms to 42s)
Available subarrays listed in APT
Output
Horizontal fast scanning direction
j
Vertical slow scanning direction
HDIR=0
VDIR=0
NCOLS Dj
NROWS Di
j0 COLCORNER
i0 ROWCORNER

## Slide 6: Non destructive “up the ramp” readout
Non destructive reads
“maintain history of integration”
Signal
idle
reset
Non destructive
reads during
integration
Time
1
2
3
12
Fit of the slope provides
the count rate
Signal
Time
1
2
3
Cosmic
ray hit
Signal
Time
1
2
3
12
Saturation
CMOS allows to monitor the accumulated charge without “erasing” it
Multiple samples averaged down the noise

## Slide 7: Integration & Exposure
One exposure can have multiple identical integrations
Signal
idle
reset
Time
reset
reset
Integration #1
Integration #2
Integration #3
idle
Exposure

## Slide 8: Data Cube
Signal
idle
reset
Non destructive
reads during
integration
Time
1
2
3
12
Time
1
2
12
Each read is saved as a slice of a 3D data cube
Getting all the reads in the ramp is the optimal situation, but
it is not always feasible

## Slide 9: Dealing with data volume
Signal
idle
reset
Non destructive
reads during
integration
Time
1
2
3
12
Time
1
2
12
11
10
11
10
3
Signal
idle
reset
Time
1
2
3
12
Time
1
2
12
11
10
11
10
3
Reads not
saved- “dropped”
Signal
idle
reset
Time
Time
1
2
12
3
4
11
10
9
Signal
idle
reset
Time
1
2
3
12
Time
1
10
11
4
9
1
2
2
3
3
Groups of reads
can be averaged
on board
“Groupgap”
“Nframes”

## Slide 10: Different instruments, different requirement, different readouts patterns
Each instrument has different number of SCAs, different requirements and different “tuning”.
Data volume restrictions also dictate readout patterns that define the structure of an integration
SI # - lco | Gain e/DN | Total Noise e-
NIRISS 1-5.3 mm | ~1.6 | ~8.5
NIRCam 8-2.5 mm 2-5.3 mm | ~ 2 | 5-6 8-8.5
NIRSpec 2-5.3 mm | ~1 (FF) ~2 (sub.) | 6-7.5 (trad) 5.3-7 (IRS2)
SI | Pattern name | Nframes | Group Gap
NIRISS | NIS-RAPID NIS | 1 4 | 0 0
NIRCam | RAPID | 1 | 0
 | BRIGHT1 BRIGHT2 | 1 2 | 1 0
 | SHALLOW2 SHALLOW4 | 2 4 | 3 1
 | MEDIUM2 MEDIUM8 | 2 8 | 8 2
 | DEEP2 DEEP8 | 2 8 | 18 12
NIRSpec | NRSRAPID NRS | 1 4 | 0 0
 | NRSIRS2RAPID NRSIRS2 | 1 5 | 0 0

## Slide 11: NIRSpec Low Noise readout : IRS2
Most NIRSpec observations are detector limited -> most stringent noise requirement
GSFC group analyzed noise properties of NIRSpec detector system and developed a new low noise readout scheme for NIRSpec Full Frame exposures.
“High level” recipe to reduce noise and noise correlation:
Send more reference pixels “to the ground” for post processing
Read reference pixels more frequently
IRS2= Improved Reference Sampling and Subtraction
Poster #3
Traditional
IRS2
Frame Time 10.7s
Frame Time 14.6s
Traditional
IRS2
Raw data
format
Processed dark
exposure

## Slide 12: Non ideal behavior to familiarize with….
These detector are the state of the art for NIR space mission with a 2018 launch
They are however not perfect:
Bad Pixels
Dead pixels
Hot/noisy pixels
RC or RTN pixels
< 0.5% on average, flagged in DQ arrays
“Cosmetics”
Variation in sensitivity
Variation in full well
Generally mitigated with dithering and reference file corrections
Non Linearity
Persistence

## Slide 13: Summary
JWST NIR instruments have state of the art H2RG detectors
ASIC SIDECAR controllers add flexibility and tuning of the performances (but also some correlated noise)
Each SI has different requirements
  They are in general met with significant margin
  Some operational aspects are different between various SIs
Some of the detector non ideal behaviors are still under full characterization and they will be corrected, mitigated and /or flagged
Ground detector labs will be operative during JWST operations to support investigation of possible issue and develop operational improvements