## Slide 1: Near-InfraRed Imager and Slitless Spectrograph: Imaging and Interferometry
Alex Fullerton
STScI / NIRISS Team Lead
OUTLINE
Introducing NIRISS
Imaging
Aperture Masking Interferometry

## Slide 2: A Bit About NIRISS
Developed / Provided By:
  Canadian Space Agency
Principle Investigator:
  Prof. René Doyon
Prime Contractor:
  Honeywell
Technical Development:
  National Research Council
  of Canada
NIRISS is packaged with the Fine Guidance Sensor.
FGS is the camera used to acquire targets and guide on them during observations. Independent functionality from NIRISS.

## Slide 3: Optical Layout of NIRISS
Efficient, All-Reflective Design
Parameter | Value
Array Size | 2048 × 2048 (2040 x 2040 active)
Pixel size | 18 μm × 18 μm
Dark rate | < 0.04 e−/s
Noise | 16.3 e− (correlated double sample)
Gain | 1.6 e− / ADU
Field of View | 2.2´ × 2.2´
Plate scale in x | 0.0654 arcsec/pixel
Plate scale in y | 0.0659 arcsec/pixel
Hawaii 2RG Detector
HgCdTe with 5.2 μm cut-off

## Slide 4: Pupil / Filter Wheel Combinations Enable Four Observation Modes
Pupil Wheel
Filter Wheel
Imaging (Imaging)
Aperture Masking Interferometry (AMI)
Wide-Field Slitless Spectroscopy (WFSS)
Single-Object Slitless Spectroscopy (SOSS)

## Slide 5: Imaging: “Blue”
Imaging: “Red”
All filters except F158M are NIRCam flight spares
All filters except F380M are NIRCam flight spares

## Slide 6: NIRISS Filter Transmission & Sensitivity
Filter | nJy | m(Vega)
F090W | 11.28 | 28.28
F115W | 11.22 | 28.06
F140M | 14.80 | 27.43
F150W | 9.19 | 27.83
F158M | 12.88 | 27.39
F200W | 7.81 | 27.54
F277W | 6.63 | 27.09
F356W | 6.89 | 26.56
F380M | 18.74 | 24.34
F430M | 28.32 | 24.65
F444W | 12.29 | 25.49
F480M | 36.85 | 24.14
S/N = 10 in 10 ks
NOTE:
These filters are very
closely matched to the
filter set of NIRCam.

## Slide 7: Caveats and Counselling
Near-IR Imaging with NIRISS:
Is an essential part of data collection in the WFSS mode; optional for AMI
Provides a powerful “parallel” capability
  Matched NIRCam filters; comparable sensitivity
  Increases areal coverage of the sky when paired with NIRCam
  Provides near-IR imaging at lower data rate than NIRCam
However: NIRCam is the JWST instrument of choice for near-IR imaging!
Twice the field of view of NIRISS
Simultaneously images “short” and “long” wavelengths
Better sampling of the PSF at wavelengths < 2.5 µm
Accordingly, the NIRISS Imaging template:
Only supports “parallel” observations
Does not support the use of subarrays
Will necessarily follow dither pattern / mosaic strategy of “primary” instrument
4× multiplex advantage
compared to NIRISS

## Slide 8: Aperture Masking Interferometry Un “ami” des astronomes
NIRISS provides the first space-based implementation of aperture masking

## Slide 9: The Non-Redundant Mask (NRM)
7 undersized apertures: ~15% throughput
n × (n−1) / 2 = 21 distances (“baselines”) between pairs of apertures
Apertures placed so that all vectors between them (angles and baselines) are unique (“non-redundant”)
80 pixels
5.2”
Oversampled ×11
Logarithmic “stretch”
Point source through F430M
Modeled by WebbPSF
NRM PSF / Interferogram
Flocon de neige / Snowflake
Terminology:

## Slide 10: AMI in [Simulated] Action
Slide courtesy of D. Thatte
AMI
Direct
Simulations Include:
Read Noise
Poisson Noise
Dark Current
Background
Flat-Field Error

## Slide 11: The Interferometric Advantage
Simulations by: Ford et al. 2014, ApJ, 783, 73
Pupil
PSF
Dynamic Range: 104:1
PSF core
Dynamic Range: 100:1
5 λ/D
0.75 λ/D
Sharper Core!

## Slide 12: A Niche for AMI
IWA NIRCam Wedge Occulter
70 mas
400 mas
Inner Working Angle @ 4.4 μm |  | 
NIRCam / Wedge | 4.0 λ/D | 560 mas
NIRISS / NRM | 0.5 λ/D | 70 mas

## Slide 13: Operational Flow of An AMI Visit
NIRISS Operations Concept Document (P. Goudfrooij et al.)
Visit 1: Science Target
Target Acquisition
Configure
Expose
Dither
Repeat with New Filter?
Obtain Reference PSFs?
Subarray
80 pixels × 80 pixels
(5.2″ × 5.2″)
Visit 2: Reference Star
Must Be Contemporaneous
Must Repeat Sequence
Used to derive
  Closure Phases
  Closure Amplitudes
Visit 1: Science Target
Target Acquisition
Visit 1: Science Target
Target Acquisition
Configure
Visit 1: Science Target
Target Acquisition
Configure
Expose
Visit 1: Science Target
Target Acquisition
Configure
Expose
Dither
Visit 1: Science Target
Target Acquisition
Configure
Expose
Dither
Repeat with New Filter?
Visit 1: Science Target
Target Acquisition
Configure
Expose
Dither
Repeat with New Filter?
Obtain Reference PSFs?
Visit 1: Science Target
Target Acquisition
Configure
Expose
Dither
Repeat with New Filter?

## Slide 14: Predicted Performance of AMI
Figure courtesy of É. Artigau (U de Montréal)

## Slide 15: Synthesis Imaging with AMI
After Ford et al. 2014, ApJ 783,73
Use Case: Structure in the Nuclei of AGN
Bar
Fainter Bar
Asymmetric Bar
Short Bar
Ring
9 × 1 pixels
Δm = 1 mag
(integrated)
9 × 1 pixels
Δm = 2 mag
(integrated)
3 × 1 pixels
Δm = 1 mag
(integrated)
3 × 1 pixels
Δm = 1 mag
(integrated)
5 pixel diameter
Δm = 1 mag
(integrated)
Multiple visits ~ 3 months apart

## Slide 16: Near-InfraRed Imager and Slitless Spectrograph: Imaging and Interferometry
SUMMARY:
NIRISS has imaging capability with a filter set closely matched to NIRCam.
  Integral part of observing sequence for WFSS; optional for AMI
  Powerful mode when used as a science “parallel”
  But otherwise you should use NIRCam for near-IR imaging
Aperture Masking Interferometry (AMI) is a powerful capability.
  Provides very high spatial resolution and good contrast
  Very stable, self-calibrating
  Can be used for synthesis imaging
  AMI is a friend! Use it!
L−734 Days and Counting!